Sniffing cable modems
Guy Martin <gmsoft@tuxicoman.be>
HackCon 4 - Feb 2009 – Oslo

---
Agenda
- What is DOCSIS ?
  - Use of DOCSIS
  - General architecture
  - Registration process
  - Encryption on the link
- How to sniff it
  - DVB-C / ATSC card
  - Packet-o-matic to the rescue

---
Agenda
- Security concerns
  - Privacy
  - Impersonating
  - Modem SNMP tricks
  - Misc
- References
  - DOCSIS
  - MPEG
  - Packet-o-matic

---
What is DOCSIS
- Use of DOCSIS
  - Internet : The most known application of the DOCSIS protocol
  - Telephony : Most cable modems have a built-in ATA (Analog Telephone Adapter)
  - Digital TV decoders : built-in cable modems to monitor/feedback data from end users (VoD)

---
What is DOCSIS
- General architecture
  - CMTS on the ISP side broadcast packets to end users on a common single frequency
  - Modems on end user side sends packets back to CMTS on another frequency during its timeslot
  - A CMTS serves from a small neighborhood to a whole city
  - Downstream frequency is in the same range than TV ones
  - Uses MPEG packets like normal digital TV to encapsulate data

---
What is DOCSIS
- Registration process
  - Aquire and lock the downstream frequency
  - Get upstream parameters from downstream
  - Get an IP address via DHCP
  - Download the modem configuration via TFTP
  - Apply the configuration and enable IP forwarding

---
What is DOCSIS
- Encryption on the link
  - Encryption and authentication are NOT mandatory
  - BPI (Baseline Privacy Interface) provides a mechanism for authentication and/or encryption
  - Triple DES is available since DOCSIS 1.0
  - Authentication using certifiates since DOCSIS 1.1
  - AES available since DOCSIS 3.0

---
How to sniff it
- DVB-C / ATSC card
  - Possible because protocols and frequencies are purposely similar to digital TV ones
  - Inexpensive
  - Only the downstream traffic can be captured
  - Different hardware like USRP could be used to capture both upstream and downstream
  - DOCSIS 3.0 uses multiple downstream frequencies

---
How to sniff it
- Packet-o-matic to the rescue
  - Input module capture the traffic
  - Packets are processed and matched using rules
  - Helper and contrack modules prepare for targets
  - Eventually the target module process the packets to produce the desired output
  - Everything occurs real-time
  - Telnet and XML-RPC interface available

---
Security concerns - Privacy
- Sniff data destinated to all ISP users
  - Reassemble streams real-time and extract useable files on the fly (mail, land line phone calls, IM conversations, …)
  - Gather personal data : Facebook chat / images, google search, other
  - User workaround :
    - use a VPN tunnel to a trusted enpoint
    - use encrypted protocols
  - ISP workaround : enable DOCSIS encryption (BPI)

---
Security concerns - Impersonating
- Send packets as someone else
  - DoS by reinjecting TCP RST (tcpkill) packets or ICMP error packets
  - Workaround : none
  - Use someone else's IP address, implies bandwidth and quota
  - User workaround : Set your firewall NOT to drop packets but rather reject them with TCP RST to kill rogue connections
  - ISP workaround : enable BPI

---
Security concerns – SNMP tricks
- Modem SNMP tricks
  - Change IP filters of the modem's ethernet bridge
  - Deny access to the server polling the download/upload quota
  - Reboot the modem
  - Anything else the modem's SNMP interface allows
  - ISP workaround : allow SNMP access only from coax interface

---
Security concerns - Misc
- Bypass filters
  - Bypass modem filters by reinjecting sniffed packets in the LAN
  - Create a virtual network interface (tap device) so other tools can be used
  - ISP workaround : enable BPI

---
Security concerns - Misc
- VoD sniffing
  - Gather VoD information from decoders traffic
  - Tune on the right frequency
  - ISP workaround :
    - encrypt VoD MPEG stream
    - enable BPI

---
References
- DOCSIS
  - http://www.cablelabs.com/
  - http://www.cablemodem.com/specifications/
- MPEG
  - ISO/IEC 13818-1
- Packet-o-matic
  - http://www.packet-o-matic.com

---
Conclusions
- Users
  - If BPI is not enabled, consider your data public
  - Encrypt as much as you can
  - Monitor your firewall for ppl who might impersonate your connection
- ISP
  - Enabling BPI is severely recommended
  - Not doing so allow users to bypass the first level of protection provided by the modem
  - Without BPI theft of service and impersonation are possible